## Slide 1
SMART CLASSROOM
IoT-Based Motion,Temperature, Humidity and Noise Monitoring
ITEE
SUMMER PROGRAM

## Slide 2
Contents
05
06
07
01
Introduction
Results
02
Problem Statement
Challenges and Future Works
03
Goals and Objectives
Conclusion
04
Tools and Methodology

## Slide 3
Meet our Team
BRIAN KIBOR
WIRELESS COMMUNICATION
PRAKASH KARKEE
COMPUTER SCIENCE AND ENGINEERING
LIHINI KARUNARATHNE
COMPUTER SCIENCE AND ENGINEERING

## Slide 4
Introduction
Classroom environments directly impact student focus, comfort, and learning outcomes.
Traditional classrooms lack automated monitoring of temperature, noise, and occupancy, making energy management and real-time supervision difficult.

## Slide 5
Amount of student attention level reduced by noise levels above 65 dB in classrooms.
Generated energy that goes to waste globally due to inefficient usage and monitoring.
30%
5% global GDP
Status Quo?
Notes: 400 exa Joules

## Slide 6
Problem Statement

## Slide 7
Uncomfortable classroom environment (temperature & noise).
Problem Statement
Energy wastage due to inefficient Lighting, AC and Heater use.
No centralized monitoring environmental conditions in real-time.
.

## Slide 8
Goals and Objectives
Develop a real-time IoT monitoring system.
Automate classroom comfort and energy efficiency.
Enable cloud-based data logging and visualization.
Notes: Collect classroom environmental data (temperature, humidity, motion, noise) using ESP32 and sensors.
Control AC and heater based on occupancy (motion) and temperature thresholds.
Push sensor data to Firebase and provide a dashboard for teachers/administrators to monitor conditions remotely.

## Slide 9
Tools and Methodology
ESP-32
ESP-32 Microcontroller for controlling the smart class room system.
Firebase and HMTL
Real time database for storing data and displaying historical statistics.
DHT11, PIR, I2S Microphone and LEDs
Sensors for collecting temperature, humidity, motion and noise levels in class room. LEDs for demonstrating Lighting, AC and Heater Control

## Slide 10
System Architecture

## Slide 11
Circuit Diagram

## Slide 12
System Logic
System
Logic

## Slide 13
Finding & Results
ESP32-based IoT system monitoring temp, humidity, motion, noise.
Automated AC/Heater control based on motion and temperature.
Firebase cloud logging for real-time dashboard.

## Slide 14
Smart Class Room
Play Video

## Slide 15
Smart Class Dashboard

## Slide 16
Insufficient memory limiting BLE integration
Integration of Teacher Notification
Machine Learning for voice activation
Challenges & Future Works

## Slide 17
Conclusion
Wi-Fi connectivity, Firebase real-time database, motion detection, temperature and humidity sensing, AC and heater control, and noise level monitoring into a smart classroom system for improved monitoring and energy conservation.

## Slide 18
Thank you
Any Questions?